## Slide 2
Normal Load (Axial load): Load is perpendicular to the
supporting material.
- Tension Load: As the ends of material are pulled apart
to make the material longer, the load is called a tension
load.
- Compression Load: As the ends of material are pushed in
to make the material smaller, the load is called
a compression load.
Tension
Compression
Classifying Loads on Materials

## Slide 3
Stress and Strain
In order to compare materials, we must have measures.
Stress : load per unit Area
F : load applied in pounds
A : cross sectional area in in²
: stress in psi
A
F
F

## Slide 4
Strain:
- Ratio of elongation of a material to the original length
- unit deformation
e : elongation (ft)
Lo : unloaded(original) length of a material (ft)
: strain (ft/ft) or (in/in)
Elongation:
L : loaded length of a material (ft)
Lo
e
L
Stress and Strain

## Slide 5
Stress-Strain Diagram
A plot of Strain vs. Stress.
The diagram gives us the behavior of the material and
material properties.
Each material produces a different stress-strain
diagram.

## Slide 6
Strain ( ) (e/Lo)
4
1
2
3
5
Stress (F/A)
Elastic
Region
Plastic
Region
Strain
Hardening
Fracture
ultimate
tensile strength
Slope=E
Elastic region
slope=Young’s(elastic) modulus
yield strength
Plastic region
ultimate tensile strength
strain hardening
fracture
necking
yield
strength
Stress-Strain Diagram

## Slide 7: Tensile

## Slide 8
Elastic Region (Point 1 –2)
- The material will return to its original shape
after the material is unloaded( like a rubber band).
- The stress is linearly proportional to the strain in
this region.
: Stress (psi)
E : Elastic modulus (Young’s Modulus) (psi)
: Strain (in/in)
Point 2 : Yield Strength : a point at which permanent
deformation occurs. ( If it is passed, the material will
no longer return to its original length.)
or
Stress-Strain Diagram

## Slide 9
Plastic Region (Point 2 –3)
- If the material is loaded beyond the yield strength,
the material will not return to its original shape
after unloading.
- It will have some permanent deformation.
- If the material is unloaded at Point 3, the curve will
proceed from Point 3 to Point 4. The slope will be
the as the slope between Point 1 and 2.
- The distance between Point 1 and 4 indicates the
amount of permanent deformation.
Stress-Strain Diagram

## Slide 10
Tensile Strength (Point 3)
- The largest value of stress on the diagram is called
Tensile Strength(TS) or Ultimate Tensile Strength
(UTS)
- It is the maximum stress which the material can
support without breaking.
Fracture (Point 5)
- If the material is stretched beyond Point 3, the stress
decreases as necking and non-uniform deformation
occur.
- Fracture will finally occur at Point 5.
Stress-Strain Diagram